## Slide 1
DESKTOP APPLICATION · PHENOTYPING PIPELINE
Plot Extractor
One clean, correctly-located image per plot — from drone survey to emergence count.
Plot Extractor · DPIRD × APPN
01

## Slide 2
THE CHALLENGE
A drone survey isn't a dataset
!
Rows get clipped.
A plot grid rarely sits exactly on the planted rows.
!
Frames don't cover a plot.
A 6 m plot is longer than one camera footprint.
!
Visible seams.
Stitching two frames leaves a brightness / contrast step.
!
Field-edge plots fail.
No near-nadir frame → smeared, black crops.
The job
Turn 3,400 overlapping oblique photos into 392 tidy, comparable, correctly-located plot images — every planted row inside, no seams, no manual cleanup.
392
plots per flight
Plot Extractor · DPIRD × APPN
02

## Slide 3
HOW IT WORKS
Boundary → best frame → tidy crop
01
Back-project
Each plot polygon projected into every camera.
02
Pick near-nadir
The sharpest, least-oblique covering frame wins.
03
Gap-fill + match
Neighbour frames fill gaps; tone matched.
04
Auto-fit rows
Detect the band; trim to exactly N rows.
05
Write
Raw + ortho crop + manifest, per plot.
Every output pixel is native raw from one frame — a single resample to make the strip upright. Far sharper than the orthomosaic, and each file is exactly one plot.
Plot Extractor · DPIRD × APPN
03

## Slide 4
KEY FEATURE
Auto-fit to the rows
The grid clips rows. So the app renders each crop wider than the boundary, detects the crop rows from the tillage-ridge pattern — working even before emergence — then snaps to exactly your row count.
✓
Recovers clipped rows — by rendering past the boundary.
✓
Recentres on the rows — width_shift mode.
✓
Reports exact area — covering the rows, in m².
Set two things
rows/plot = 7 · mode = width_shift
7
rows, every plot. Per-trial — set 0 to auto-detect.
Plot Extractor · DPIRD × APPN
04

## Slide 5
UNDER THE HOOD
Built to be hands-off
Near-nadir scoring
Prefers the sharpest, least-foreshortened covering frame.
Gap-fill
One pixel = one frame; neighbours fill only the holes.
Affine seam-match
Mean + contrast matched — invisible joins, native pixels.
Ortho fallback
Edge plots auto-rebuilt from the ortho; white nodata → black.
Chunk aware
Reads a project's sub-projects; Day 1 vs Day 2 in one click.
GPU + parallel
GPU compute, multi-core image stage — 392 plots in minutes.
Plot Extractor · DPIRD × APPN
05

## Slide 6
WHAT YOU GET
A dataset, plus its provenance
Per run
RawCrops\ — sharp upright plot images OrthoCrops\ — deskewed nadir crops manifest.csv — one row per plot
Every crop is accountable
The manifest records coverage, frames used, seam location, detected rows and the exact fitted area in m² — and flags any plot rebuilt from the ortho. Nothing is a black box.
Raw fidelity kept: natural per-plot brightness is preserved for downstream per-plot adaptive thresholding — the most raw image possible.
Plot Extractor · DPIRD × APPN
06

## Slide 7
GETTING STARTED
Three settings and go
1
Pick the chunk
Project, chunk, plot shapefile, raw folder, output.
2
Auto-fit = 7 rows
Rectified style · width_shift · sRGB on.
3
Run
Test with Limit = 10, then run the full trial.
A full run of raw + ortho self-corrects seams, edge plots and nodata — no post-processing. See the User Guide for every field.
Plot Extractor · DPIRD × APPN
07